## Slide 1: Chrono support for Human-in-the-Loop simulation
Speaker: Kyle Sha
(Simulation-Based Engineering Lab)
University of Wisconsin - Madison
1

## Slide 2: Overview of the human-in-the-loop tutorial
Human-in-the-loop = the simulation runs at wall-clock speed and a person closes the control loop
In this tutorial, you will learn how to
  PART 1: Keep a Chrono::Vehicle simulation real-time and measure how well you did
  PART 2: Put a human on the keyboard with ChInteractiveDriver
  PART 4: Bring a device Chrono doesn't know about, and close the loop back to it
  Parts 3 and 5 (gamepad/wheel, vehicle picker, overlay flags) are in the repo - no time today
Everything runs in PyChrono; no special hardware is required
The whole human-in-the-loop contract is: spin once per step, three floats in, state out
University of Wisconsin - Madison
2

## Slide 3: Before we start ......
This is a walkthrough - nothing to install right now; everything runs on my machine
Code, slides and a written walkthrough: github.com/ksha23/chrono-hil-tutorial
To run it yourself afterward:
  conda create -n chrono_hil -c projectchrono -c conda-forge pychrono pygame python=3.13
  conda activate chrono_hil
Do NOT pip install pychrono - the PyPI package with that name is an unrelated library
python tutorial_HIL_driver.py opens an Irrlicht window with an HMMWV - drive it with the arrow keys
All switches are in the CONFIGURATION section at the bottom of tutorial_HIL_driver.py
University of Wisconsin - Madison
3

## Slide 4: Part 1: Keep the simulation real-time
University of Wisconsin - Madison
4

## Slide 5: What "real-time" means in Chrono
Chrono integrates as fast as it can; it has no notion of wall-clock time by itself
Real Time Factor: RTF = compute time for a step / step size
  RTF < 1: faster than real time - we must WAIT after each step
  RTF > 1: slower than real time - nothing can be done except a cheaper model or a bigger step
Soft real-time: spin after each step until wall time catches up with simulation time
  No OS scheduling guarantees; good enough for a driving simulator, not for a control ECU
Three equivalent mechanisms in PyChrono (next slides): ChRealtimeStepTimer, ChVehicle.EnableRealtime, or your own
University of Wisconsin - Madison
5

## Slide 6: Step 1: The simulation loop (Lines 376 to 404)
while vis.Run():
sim_time = system.GetChTime()
# Render scene
if step_number % render_steps == 0:
vis.BeginScene()
vis.Render()
vis.EndScene()
# PART 4: sample the device ONCE per step and hold it for the step
if device is not None:
smoother.set_target(*device.poll())
smoother.advance(step_size)
smoother.apply_to(driver)
# Get driver inputs (three floats) - this is the whole human-in-the-loop contract
driver_inputs = driver.GetInputs()
# Update modules (process inputs from other modules)
driver.Synchronize(sim_time)
terrain.Synchronize(sim_time)
vehicle_model.Synchronize(sim_time, driver_inputs, terrain)
vis.Synchronize(sim_time, driver_inputs)
# Advance simulation for one timestep for all modules
driver.Advance(step_size)
terrain.Advance(step_size)
vehicle_model.Advance(step_size) # spins here if REALTIME == "vehicle"
vis.Advance(step_size)
Synchronize: every module reads what it needs from the others at time t
Advance: every module integrates from t to t + step
The driver is queried BEFORE Synchronize - inputs are sampled once and held for the step
University of Wisconsin - Madison
6

## Slide 7: Step 2: Measure it - sim time vs wall time (Lines 406 to 412)
# Console report: how far is the sim from wall time?
if step_number % report_steps == 0:
wall = time.perf_counter() - wall_start
print(f"{sim_time:7.2f} {wall:7.2f} {wall - sim_time:+7.3f} {vehicle.GetRTF():6.2f}"
f" {vehicle.GetSpeed():7.2f} {driver_inputs.m_steering:6.2f}"
f" {driver_inputs.m_throttle:5.2f} {driver_inputs.m_braking:5.2f}")
drift = wall time - simulation time: negative means the sim is ahead of the clock
vehicle.GetRTF() is the true RTF of the last step, even when real time is enforced
University of Wisconsin - Madison
7

## Slide 8: Show Time
REALTIME = "none": watch the drift column run away
Change step_size to 5e-4 - RTF goes above 1 and the sim can never be real-time
University of Wisconsin - Madison
8

## Slide 9: Step 3: Enforce real time, three ways (Lines 357 to 362)
# Real-time setup (PART 1)
# -----------------------------------------------------------------------
if REALTIME == "vehicle":
vehicle.EnableRealtime(True)
rt_timer = chrono.ChRealtimeStepTimer() # used when REALTIME == "per_step"
cum_timer = CumulativeRealtimeTimer() # used when REALTIME == "cumulative"
"vehicle": ChVehicle::EnableRealtime(True) spins inside vehicle.Advance() using a ChRealtimeStepTimer
"per_step": the same timer, called explicitly at the end of the loop (next slide)
"cumulative": our own timer that compares total simulated time to total wall time
University of Wisconsin - Madison
9

## Slide 10: Step 4: A drift-free timer in 10 lines (Lines 56 to 74)
class CumulativeRealtimeTimer:
"""Soft real-time that does not accumulate drift.
ChRealtimeStepTimer measures each step independently: any time lost on a
slow step (or spent in Python between steps) is never recovered. This timer
instead compares the *total* simulated time with the *total* wall time, so a
slow step is followed by a few fast steps that catch back up.
"""
def __init__(self):
self.reset()
def reset(self):
self.t_start = time.perf_counter()
def spin(self, sim_time):
while time.perf_counter() - self.t_start < sim_time:
pass # spin in place until real time catches up
Compare TOTAL simulated time with TOTAL wall time - lost time is caught up on the next fast steps
This is how driving simulators (e.g. Chrono::HIL) keep their clock; the same idea also works across processes
University of Wisconsin - Madison
10

## Slide 11: Show Time
Measured on a laptop, HMMWV + TMeasy tires, step 3 ms (RTF ~ 0.14):
  "none": drift -69 s after 17 s of wall time
  "per_step": drift +0.012 s after 17 s and growing
  "vehicle": drift +0.021 s after 17 s and growing
  "cumulative": drift +0.000 s
Drift matters more the closer you are to RTF = 1
University of Wisconsin - Madison
11

## Slide 12: Part 2: A human on the keyboard
University of Wisconsin - Madison
12

## Slide 13: Step 1: ChInteractiveDriver (Lines 296 to 307)
elif INPUT_SOURCE == "keyboard":
### PART 2: keyboard through the Irrlicht window ###
# Arrow keys steer/accelerate/brake, 'C' centers steering, 'R' releases
# the pedals, 'L' locks the current inputs.
driver = veh.ChInteractiveDriver(vehicle)
steering_time = 1.0 # time to go from 0 to +1 (or from 0 to -1)
throttle_time = 1.0 # time to go from 0 to +1
braking_time = 0.3 # time to go from 0 to +1
driver.SetSteeringDelta(render_step_size / steering_time)
driver.SetThrottleDelta(render_step_size / throttle_time)
driver.SetBrakingDelta(render_step_size / braking_time)
driver.SetGains(4.0, 4.0, 4.0) # first-order lag from key target to applied input
Arrow keys steer/accelerate/brake, C centers steering, R releases the pedals, L locks the inputs
Each keypress moves a TARGET by "delta"; the applied input follows the target with a first-order lag (SetGains)
delta = render_step / time-to-full-scale: full steering lock takes 1 s, full braking 0.3 s
University of Wisconsin - Madison
13

## Slide 14: Step 2: Route the window events to the driver (Lines 339 to 342)
vis.AddSkyBox()
vis.AttachVehicle(vehicle)
if INPUT_SOURCE in ("keyboard", "gamepad"):
vis.AttachDriver(driver) # route Irrlicht key/joystick events to the driver
The Irrlicht visual system owns the keyboard; AttachDriver forwards key events to the driver
Nothing else in the loop changes - the driver still just returns three floats
The same driver reads a gamepad or wheel natively - SetInputMode(JOYSTICK), presets ship with Chrono
University of Wisconsin - Madison
14

## Slide 15: Show Time
Driving the HMMWV with the arrow keys - watch the Irrlicht HUD (speed, inputs, RTF)
University of Wisconsin - Madison
15

## Slide 16: Part 4: A device Chrono doesn't know about, and closing the loop
a UDP console, a gamepad, a steering wheel, a phone, another process...
University of Wisconsin - Madison
16

## Slide 17: Part 4's architecture: two processes, one UDP contract
Operator machine
operator_console.py
Simulation machine
tutorial_HIL_driver.py
→ steering, throttle, braking
speed, RTF, lateral accel ←
Both directions are plain UDP datagrams - two processes, possibly two machines, no shared memory. The grey arrow only fires when SEND_FEEDBACK = True.
University of Wisconsin - Madison
17

## Slide 18: The human-in-the-loop contract
A driver is just three floats per step: steering [-1, 1], throttle [0, 1], braking [0, 1]
veh.ChDriver is the plain container: SetSteering(), SetThrottle(), SetBraking()
So the recipe for ANY device is:
  1. poll the device (never block the physics loop)
  2. rate-limit / smooth (a human arm is not a step function)
  3. write into the ChDriver once per step - zero-order hold until the next step
Today: a UDP operator console in a second terminal - the operator side has no Chrono dependency at all
University of Wisconsin - Madison
18

## Slide 19: Step 1: A UDP input source (Lines 136 to 169)
class UdpInput:
"""Receive 'steering,throttle,braking' text datagrams from an operator.
Run operator_console.py in another terminal (or on another machine) and
drive with the arrow keys there. The socket is non-blocking: the physics
loop never waits for the operator. If no packet arrived since the last
step, the previous target is held (zero-order hold).
"""
def __init__(self, port=9870):
self.sock = socket.socket(socket.AF_INET, socket.SOCK_DGRAM)
self.sock.bind(("0.0.0.0", port))
self.sock.setblocking(False)
self.operator_addr = None
self.last = (0.0, 0.0, 0.0)
self.packets = 0
print(f"[udp] listening on port {port} - start operator_console.py")
def poll(self):
# Drain everything that is queued and keep only the newest packet
while True:
try:
data, addr = self.sock.recvfrom(256)
except BlockingIOError:
break
try:
s, t, b = (float(x) for x in data.decode().split(","))
self.last = (s, t, b)
self.operator_addr = addr
self.packets += 1
except ValueError:
pass
return self.last
Non-blocking socket, drained every step; the newest packet wins, an empty queue holds the last value
The operator can be anywhere on the network - and the console has no Chrono dependency at all
University of Wisconsin - Madison
19

## Slide 20: Step 2: Sample once per step, then hold (Lines 384 to 393)
# PART 4: sample the device ONCE per step and hold it for the step
if device is not None:
smoother.set_target(*device.poll())
smoother.advance(step_size)
smoother.apply_to(driver)
# Get driver inputs (three floats) - this is the whole human-in-the-loop contract
driver_inputs = driver.GetInputs()
poll -> smooth -> write, then GetInputs() as before; the physics loop never waits on the device
University of Wisconsin - Madison
20

## Slide 21: Step 3: Send state back at render rate (Lines 413 to 417)
# PART 4: feedback to the operator (speed, RTF, lateral acceleration, applied inputs)
if SEND_FEEDBACK and device is not None and step_number % render_steps == 0:
acc = vehicle.GetPointAcceleration(chrono.ChVector3d(0, 0, 0))
device.send_feedback(f"{sim_time:.3f},{vehicle.GetSpeed():.3f},{vehicle.GetRTF():.3f},{acc.y:.3f},"
f"{driver_inputs.m_steering:.3f},{driver_inputs.m_throttle:.3f},{driver_inputs.m_braking:.3f}")
Speed, RTF and lateral acceleration go back to whoever sent us inputs (UdpInput remembers the address)
Send at render rate (50 Hz), not at every physics step - the human cannot use 333 Hz
University of Wisconsin - Madison
21

## Slide 22: Show Time
Two terminals on one laptop over localhost - or two machines over the network, same code either way
SEND_FEEDBACK = True: speed, RTF and lateral acceleration come back to the console while you drive
Stop the console mid-drive: the last input is held - what should a real simulator do here?
University of Wisconsin - Madison
22

## Slide 23: Where this goes next
Chrono::HIL (github.com/zzhou292/chrono-HIL): the same three-float interface, scaled up
  SDL steering wheels with force feedback, cumulative real-time timer, multi-vehicle traffic
  ROS 2 and Unity bridges, teleoperation over the network, deformable (SCM) terrain
Chrono::Sensor: cameras/lidar rendered from the vehicle for the operator's screen
Chrono::Synchrono: several humans in the same world, each on their own machine
Takeaways
  Real time in Chrono is soft: spin once per step, and measure the drift
  The human interface is three floats per step, sampled once and smoothed
  Never let the input device block the physics loop
University of Wisconsin - Madison
23

## Slide 24: Any questions?
University of Wisconsin - Madison
24

## Slide 25
Thank you.
kasha2@wisc.edu
Simulation-Based Engineering Lab
University of Wisconsin - Madison
Lab website: http://sbel.wisc.edu
Chrono website: http://www.projectchrono.org
Source code: https://github.com/projectchrono
Tutorial code + slides: https://github.com/ksha23/chrono-hil-tutorial
University of Wisconsin - Madison
25