## Slide 1: Chrono support for Human-in-the-Loop simulation
Speaker: Kyle Sha
(Simulation-Based Engineering Lab)
University of Wisconsin - Madison
1

## Slide 2: Why put a human in the loop at all?
start with a task that no controller in this tutorial can do for you
University of Wisconsin - Madison
2

## Slide 3: A load on a cable, and a pad to put it on
A gantry crane: four rigid bodies, two speed motors, and a payload hanging on a distance constraint
  no Chrono::Vehicle anywhere in it, and no autopilot either
Steering drives the trolley across, throttle and braking drive it along the rail
  the load then does whatever physics says, and it swings, with nothing to damp it but you
The task: set it down on the green pad with the swing under 2 degrees
  the console prints the swing angle and how far the load is from the pad
It is genuinely hard, and that difficulty is the entire argument for putting a human in a simulation loop
University of Wisconsin - Madison
3

## Slide 4: Show Time
PLANT = "crane", INPUT_SOURCE = "udp" - the operator console in a second terminal
Watch what the operator is doing: leading the swing, not chasing it. No controller here is doing that
Nothing on screen is vehicle-specific. So what does Chrono actually require of a human interface?
University of Wisconsin - Madison
4

## Slide 5: What Chrono actually requires of a human interface (Lines 151 to 178)
class DriverInputs:
"""The whole ChDriver contract, in Python."""
def __init__(self):
self.m_steering = 0.0
self.m_throttle = 0.0
self.m_braking = 0.0
def SetSteering(self, v):
self.m_steering = v
def SetThrottle(self, v):
self.m_throttle = v
def SetBraking(self, v):
self.m_braking = v
def GetInputs(self):
return self
Three floats per step: steering [-1, 1], throttle [0, 1], braking [0, 1]
veh.ChDriver is the same container in C++; this Python stand-in is what the rover and the crane use
That is the entire contract. Everything else in this talk is about filling it in, on time, from somewhere real
University of Wisconsin - Madison
5

## Slide 6: Two hard parts, and a lot that follows
Filling in three floats is easy. Two things around it are not, and both are the transferable part:
  PART 1: keeping the simulation running at wall-clock speed, and knowing when it isn't
  PART 4: taking input from a device Chrono has never heard of, and closing the loop back to it
In between, the easy case: PART 2, a human on the keyboard, which Chrono already does for you
At the end, how far the same loop stretches: gear (6), the Mcity digital twin (7), rover and crane (8)
  Parts 3 and 5 - gamepad/wheel, vehicle picker, overlay flags - are in the repo; no time today
Everything runs in PyChrono; no special hardware is required
University of Wisconsin - Madison
6

## Slide 7: Before we start ......
This is a walkthrough - nothing to install right now; everything runs on my machine
Code, slides and a written walkthrough: github.com/ksha23/chrono-hil-tutorial
To run it yourself afterward:
  conda create -n chrono_hil -c projectchrono -c conda-forge pychrono pygame python=3.13
  conda activate chrono_hil
Do NOT pip install pychrono - the PyPI package with that name is an unrelated library
python tutorial_HIL_driver.py opens an Irrlicht window with an HMMWV - drive it with W/A/S/D
All switches are in the CONFIGURATION section at the bottom of tutorial_HIL_driver.py
University of Wisconsin - Madison
7

## Slide 8: Hard part 1: keep the simulation real-time
University of Wisconsin - Madison
8

## Slide 9: What "real-time" means in Chrono
Chrono integrates as fast as it can; it has no notion of wall-clock time by itself
Real Time Factor: RTF = compute time for a step / step size
  RTF < 1: faster than real time - we must WAIT after each step
  RTF > 1: slower than real time - nothing can be done except a cheaper model or a bigger step
Soft real-time: spin after each step until wall time catches up with simulation time
  No OS scheduling guarantees; good enough for a driving simulator, not for a control ECU
Three equivalent mechanisms in PyChrono: ChRealtimeStepTimer, ChVehicle.EnableRealtime, or your own
University of Wisconsin - Madison
9

## Slide 10: The loop, and where the driver is queried (Lines 700 to 751)
while vis.Run():
sim_time = system.GetChTime()
# Render scene
if step_number % render_steps == 0:
follow_camera()
vis.BeginScene()
vis.Render()
vis.EndScene()
# PART 4 samples the device here; PART 6 applies any gear command
...
# Get driver inputs (three floats) - the whole human-in-the-loop contract
driver_inputs = driver.GetInputs()
# PART 8: hand the three numbers to whatever is being controlled
plant.apply(driver_inputs)
# Update modules (process inputs from other modules)
driver.Synchronize(sim_time)
terrain.Synchronize(sim_time)
plant.synchronize(sim_time, driver_inputs)
vis.Synchronize(sim_time, driver_inputs)
# Advance simulation for one timestep for all modules
driver.Advance(step_size)
terrain.Advance(step_size)
plant.advance(step_size) # spins here if REALTIME == "vehicle"
system.DoStepDynamics(step_size) # only for a plant that does not step itself
vis.Advance(step_size)
Synchronize: every module reads what it needs from the others at time t. Advance: every module integrates t to t + step
The driver is queried BEFORE Synchronize - the human's input is sampled once and held for the whole step
University of Wisconsin - Madison
10

## Slide 11: Measure it: sim time vs wall time (Lines 753 to 769)
# Console report: how far is the sim from wall time?
if step_number % report_steps == 0:
wall = time.perf_counter() - wall_start
# A ChVehicle measures its own real-time factor per step. The rover
# and the crane do not, so it is measured here over the reporting
# interval instead: same quantity, coarser sampling.
if vehicle:
rtf = vehicle.GetRTF()
else:
d_wall = wall - last_wall
d_sim = sim_time - last_sim
rtf = (d_wall / d_sim) if d_sim > 0 else 0.0
last_wall, last_sim = wall, sim_time
print(f"{sim_time:7.2f} {wall:7.2f} {wall - sim_time:+7.3f} {rtf:6.2f}"
f" {plant.speed():7.2f} {driver_inputs.m_steering:6.2f}"
f" {driver_inputs.m_throttle:5.2f} {driver_inputs.m_braking:5.2f}"
f" {plant.status()}")
drift = wall time - simulation time: negative means the sim is ahead of the clock
vehicle.GetRTF() is the true RTF of the last step, even when real time is being enforced
A rover or a crane has no GetRTF(), so the same number is measured here over the reporting interval
University of Wisconsin - Madison
11

## Slide 12: Show Time
REALTIME = "none": watch the drift column run away
Change step_size to 5e-4 - RTF goes above 1 and the sim can never be real-time, whatever the timer does
University of Wisconsin - Madison
12

## Slide 13: Enforce real time, three ways (Lines 657 to 671, 71 to 88)
# Real-time setup (PART 1)
realtime_mode = REALTIME
if REALTIME == "vehicle":
if vehicle:
vehicle.EnableRealtime(True)
else:
# PART 8: there is no vehicle to do the spinning, so fall back to
# the timer that does the same thing from outside.
realtime_mode = "per_step"
rt_timer = chrono.ChRealtimeStepTimer() # used when REALTIME == "per_step"
cum_timer = CumulativeRealtimeTimer() # used when REALTIME == "cumulative"
# ... and the third option, defined at the top of the file:
class CumulativeRealtimeTimer:
"""Soft real-time that does not accumulate drift.
ChRealtimeStepTimer measures each step independently: any time lost on a
slow step (or spent in Python between steps) is never recovered. This timer
instead compares the *total* simulated time with the *total* wall time, so a
slow step is followed by a few fast steps that catch back up.
"""
def reset(self):
self.t_start = time.perf_counter()
def spin(self, sim_time):
while time.perf_counter() - self.t_start < sim_time:
pass # spin in place until real time catches up
"vehicle" spins inside vehicle.Advance(); "per_step" is the same timer called explicitly; "cumulative" is ours
Per-step timers never recover time lost on a slow step. Comparing TOTAL sim time to TOTAL wall time does
University of Wisconsin - Madison
13

## Slide 14: Show Time
Measured on a laptop, HMMWV + TMeasy tires, step 3 ms (RTF ~ 0.14):
  "none": drift -69 s after 17 s of wall time
  "per_step": drift +0.012 s after 17 s and growing
  "vehicle": drift +0.021 s after 17 s and growing
  "cumulative": drift +0.000 s
Drift matters more the closer you are to RTF = 1
University of Wisconsin - Madison
14

## Slide 15: Getting a human's input in
the easy case: a device Chrono already knows about
University of Wisconsin - Madison
15

## Slide 16: The keyboard, and the free gear keys (Lines 535 to 572, 615 to 618)
elif INPUT_SOURCE == "keyboard":
### PART 2: keyboard through the Irrlicht window ###
# W/A/S/D drive, 'C' centers steering, 'R' releases the pedals, 'L' locks
# the inputs. ARROW keys are the chase camera, not driving controls.
driver = veh.ChInteractiveDriver(vehicle)
steering_time = 1.0 # time to go from 0 to +1 (or from 0 to -1)
throttle_time = 1.0 # time to go from 0 to +1
braking_time = 0.3 # time to go from 0 to +1
driver.SetSteeringDelta(render_step_size / steering_time)
driver.SetThrottleDelta(render_step_size / throttle_time)
driver.SetBrakingDelta(render_step_size / braking_time)
driver.SetGains(4.0, 4.0, 4.0) # first-order lag from key target to applied input
# ... and then, when the Irrlicht window is built:
vis.AddSkyBox()
plant.attach(vis)
if INPUT_SOURCE in ("keyboard", "gamepad"):
vis.AttachDriver(driver) # route Irrlicht key/joystick events to the driver
Each keypress moves a TARGET by "delta"; the applied input follows it with a first-order lag (SetGains)
AttachDriver forwards the window's key events - and binds Chrono's own gear keys Z X T [ ] without a line of your code
The same driver reads a gamepad or wheel natively: SetInputMode(JOYSTICK), presets ship with Chrono
University of Wisconsin - Madison
16

## Slide 17: Show Time
Driving the HMMWV with W/A/S/D - watch the Irrlicht HUD (speed, inputs, RTF)
T then [: take an automatic out of auto and hold a gear through a corner. Nothing was written to get that
University of Wisconsin - Madison
17

## Slide 18: Hard part 2: a device Chrono doesn't know about
a UDP console, a phone, a motion platform, another process, another machine...
University of Wisconsin - Madison
18

## Slide 19: Two processes, one UDP contract
Both directions are plain UDP datagrams - two processes, possibly two machines, no shared memory. The return arrow only fires when SEND_FEEDBACK = True.
Operator machine
operator_console.py
Simulation machine
tutorial_HIL_driver.py
→ steering, throttle, braking, gear
speed, RTF, lateral accel, gear ←
University of Wisconsin - Madison
19

## Slide 20: A UDP input source (Lines 219 to 269)
class UdpInput:
"""Receive 'steering,throttle,braking[,gear]' datagrams from an operator.
Non-blocking: the physics loop never waits. No packet since the last step
means the previous target is held (zero-order hold)."""
def __init__(self, port=9870):
self.sock = socket.socket(socket.AF_INET, socket.SOCK_DGRAM)
self.sock.bind(("0.0.0.0", port))
self.sock.setblocking(False)
self.operator_addr = None
self.last = (0.0, 0.0, 0.0)
self.gear_commands = []
def poll(self):
# Drain everything queued and keep only the newest packet. Gear commands
# are the exception: they accumulate, because dropping one loses a shift.
while True:
try:
data, addr = self.sock.recvfrom(256)
except BlockingIOError:
break
fields = data.decode().split(",")
if len(fields) < 3:
continue
try:
s, t, b = (float(x) for x in fields[:3])
except ValueError:
continue
self.last = (s, t, b)
self.operator_addr = addr
if len(fields) > 3 and fields[3] and fields[3] != "-": # PART 6
self.gear_commands.append(fields[3][0])
return self.last
Non-blocking socket, drained every step: the newest packet wins, and an empty queue holds the last value
The operator can be anywhere on the network, and the console has no Chrono dependency at all
University of Wisconsin - Madison
20

## Slide 21: Sample once, hold, then send state back (Lines 710 to 722, 771 to 781)
# PART 4: sample the device ONCE per step and hold it for the step
if device is not None:
smoother.set_target(*device.poll())
smoother.advance(step_size)
smoother.apply_to(driver)
# PART 6: gear commands are events, not levels, so they are applied
# once each rather than held like the three numbers above.
if gearbox is not None:
for command in device.take_gear_commands():
gearbox.command_char(command)
# Get driver inputs (three floats) - this is the whole human-in-the-loop contract
driver_inputs = driver.GetInputs()
# ... and at the end of the same step:
# PART 4: feedback to the operator (speed, RTF, lateral acceleration, applied
# inputs, and since PART 6 the gear)
if SEND_FEEDBACK and device is not None and step_number % render_steps == 0:
acc = (vehicle.GetPointAcceleration(chrono.ChVector3d(0, 0, 0)).y
if vehicle else 0.0)
rtf = vehicle.GetRTF() if vehicle else 0.0
gear = gearbox.describe() if gearbox else plant.status() or "--"
device.send_feedback(
f"{sim_time:.3f},{plant.speed():.3f},{rtf:.3f},{acc:.3f},"
f"{driver_inputs.m_steering:.3f},{driver_inputs.m_throttle:.3f},"
f"{driver_inputs.m_braking:.3f},{gear}")
poll -> smooth -> write, then GetInputs() as before; the physics loop never waits on the device
Feedback goes back at render rate (50 Hz), not every physics step - the human cannot use 333 Hz
University of Wisconsin - Madison
21

## Slide 22: Show Time
Two terminals on one laptop over localhost - or two machines over the network, same code either way
SEND_FEEDBACK = True: speed, RTF and lateral acceleration come back to the console while you drive
Stop the console mid-drive: the last input is held - what should a real simulator do here?
University of Wisconsin - Madison
22

## Slide 23: How far this goes: gear, ground, and plant
PART 6 - change gear. A gear is not a fourth float: it belongs to the vehicle, not to the driver
  the keyboard binds Z X T [ ] for free once AttachDriver is called; a socket needs an adapter and a 4th field
  a level is held, an event is drained - one press of ']' is one upshift, not "keep upshifting"
PART 7 - drive somewhere real. SCENE = "mcity" puts the car in the Mcity digital twin
  road surface as a collision mesh, 860 scenery placements over 230 meshes, MCITY_DETAIL trades scenery for frame rate
PART 8 - control something that isn't a car. PLANT = "rover" or "crane"
  the crane has no Chrono::Vehicle at all, and the payload swings with nothing to damp it but the operator
All three ride the same loop, the same three numbers, and the same operator console, unchanged
University of Wisconsin - Madison
23

## Slide 24: Where this goes next
Chrono::HIL (github.com/zzhou292/chrono-HIL): the same three-float interface, scaled up
  SDL steering wheels with force feedback, cumulative real-time timer, multi-vehicle traffic
  ROS 2 and Unity bridges, teleoperation over the network, deformable (SCM) terrain
Chrono::Sensor: cameras/lidar rendered from the vehicle for the operator's screen
Chrono::Synchrono: several humans in the same world, each on their own machine
Takeaways
  Real time in Chrono is soft: spin once per step, and measure the drift
  The human interface is three floats per step, sampled once and smoothed
  Never let the input device block the physics loop
  Levels are held, events are drained - a gear is an event
  Nothing in the pattern needs a vehicle: swap the plant, keep the loop
University of Wisconsin - Madison
24

## Slide 25: Any questions?
University of Wisconsin - Madison
25

## Slide 26
Thank you.
kasha2@wisc.edu
Simulation-Based Engineering Lab
University of Wisconsin - Madison
Lab website: http://sbel.wisc.edu
Chrono website: http://www.projectchrono.org
Source code: https://github.com/projectchrono
Tutorial code + slides: https://github.com/ksha23/chrono-hil-tutorial
University of Wisconsin - Madison
26