## Slide 1: Chrono support for Human-in-the-Loop simulation
Speaker: Kyle Sha
(Simulation-Based Engineering Lab)
University of Wisconsin - Madison
1

## Slide 2: One loop, three variables
Every human-in-the-loop simulation in this tutorial is the same loop:
  read three numbers from the human -> push them into a model -> step it -> wait for real time -> send some numbers back
What changes from part to part is not the loop. It is three variables around it:
  WHERE THE NUMBERS COME FROM - a keyboard, a wheel, a socket, another machine
  WHAT THEY DRIVE - a Chrono::Vehicle, a Viper rover, a gantry crane with a swinging load
  WHERE IT HAPPENS - a 200 x 200 m patch, or the Mcity digital twin
The invariant is worth more than any of the variables, so we start there and then change one thing at a time
University of Wisconsin - Madison
2

## Slide 3: Before we start ......
This is a walkthrough - nothing to install right now; everything runs on my machine
Code, slides and a written walkthrough: github.com/ksha23/chrono-hil-tutorial
To run it yourself afterward:
  conda create -n chrono_hil -c projectchrono -c conda-forge pychrono pygame python=3.13
  conda activate chrono_hil
Do NOT pip install pychrono - the PyPI package with that name is an unrelated library
python tutorial_HIL_driver.py opens an Irrlicht window with an HMMWV - drive it with W/A/S/D
All switches are in the CONFIGURATION section at the bottom of tutorial_HIL_driver.py
University of Wisconsin - Madison
3

## Slide 4: The invariant: one loop
University of Wisconsin - Madison
4

## Slide 5: The loop, and where the driver is queried (Lines 700 to 751)
while vis.Run():
sim_time = system.GetChTime()
# Render scene
if step_number % render_steps == 0:
follow_camera()
vis.BeginScene()
vis.Render()
vis.EndScene()
# PART 4 samples the device here; PART 6 applies any gear command
...
# Get driver inputs (three floats) - the whole human-in-the-loop contract
driver_inputs = driver.GetInputs()
# PART 8: hand the three numbers to whatever is being controlled
plant.apply(driver_inputs)
# Update modules (process inputs from other modules)
driver.Synchronize(sim_time)
terrain.Synchronize(sim_time)
plant.synchronize(sim_time, driver_inputs)
vis.Synchronize(sim_time, driver_inputs)
# Advance simulation for one timestep for all modules
driver.Advance(step_size)
terrain.Advance(step_size)
plant.advance(step_size) # spins here if REALTIME == "vehicle"
system.DoStepDynamics(step_size) # only for a plant that does not step itself
vis.Advance(step_size)
Synchronize: every module reads what it needs from the others at time t. Advance: every module integrates t to t + step
Nothing below while vis.Run(): branches on which part of the tutorial you are on. That is the point of this slide
University of Wisconsin - Madison
5

## Slide 6: What Chrono actually requires of a human interface (Lines 151 to 178)
class DriverInputs:
"""The whole ChDriver contract, in Python."""
def __init__(self):
self.m_steering = 0.0
self.m_throttle = 0.0
self.m_braking = 0.0
def SetSteering(self, v):
self.m_steering = v
def SetThrottle(self, v):
self.m_throttle = v
def SetBraking(self, v):
self.m_braking = v
def GetInputs(self):
return self
Three floats per step: steering [-1, 1], throttle [0, 1], braking [0, 1]
veh.ChDriver is the same container in C++; this Python stand-in is what the rover and the crane use
That is the entire contract. Everything else in this talk is about filling it in, on time, from somewhere real
University of Wisconsin - Madison
6

## Slide 7: What "real-time" means in Chrono
Chrono integrates as fast as it can; it has no notion of wall-clock time by itself
Real Time Factor: RTF = compute time for a step / step size
  RTF < 1: faster than real time - we must WAIT after each step
  RTF > 1: slower than real time - nothing can be done except a cheaper model or a bigger step
Soft real-time: spin after each step until wall time catches up with simulation time
  No OS scheduling guarantees; good enough for a driving simulator, not for a control ECU
Three equivalent mechanisms in PyChrono: ChRealtimeStepTimer, ChVehicle.EnableRealtime, or your own
University of Wisconsin - Madison
7

## Slide 8: Enforce real time, and measure the drift (Lines 657 to 671, 753 to 769)
# Real-time setup (PART 1)
realtime_mode = REALTIME
if REALTIME == "vehicle":
if vehicle:
vehicle.EnableRealtime(True)
else:
# PART 8: there is no vehicle to do the spinning, so fall back to
# the timer that does the same thing from outside.
realtime_mode = "per_step"
rt_timer = chrono.ChRealtimeStepTimer() # used when REALTIME == "per_step"
cum_timer = CumulativeRealtimeTimer() # used when REALTIME == "cumulative"
# ... and once per simulated second, the report that tells you if it worked:
# Console report: how far is the sim from wall time?
if step_number % report_steps == 0:
wall = time.perf_counter() - wall_start
...
print(f"{sim_time:7.2f} {wall:7.2f} {wall - sim_time:+7.3f} {rtf:6.2f}"
"vehicle" spins inside vehicle.Advance(); "per_step" is the same timer called explicitly; "cumulative" compares totals
A plant with no ChVehicle has nothing to spin for it and no GetRTF(), so both fall back to doing it from outside
University of Wisconsin - Madison
8

## Slide 9: Show Time
Measured on a laptop, HMMWV + TMeasy tires, step 3 ms (RTF ~ 0.14):
  "none": drift -69 s after 17 s of wall time
  "per_step": drift +0.012 s after 17 s and growing
  "vehicle": drift +0.021 s after 17 s and growing
  "cumulative": drift +0.000 s
Drift matters more the closer you are to RTF = 1
University of Wisconsin - Madison
9

## Slide 10: Variable 1: where the numbers come from
University of Wisconsin - Madison
10

## Slide 11: The keyboard, which Chrono reads for you (Lines 535 to 572, 615 to 618)
elif INPUT_SOURCE == "keyboard":
### PART 2: keyboard through the Irrlicht window ###
# W/A/S/D drive, 'C' centers steering, 'R' releases the pedals, 'L' locks
# the inputs. ARROW keys are the chase camera, not driving controls.
driver = veh.ChInteractiveDriver(vehicle)
steering_time = 1.0 # time to go from 0 to +1 (or from 0 to -1)
throttle_time = 1.0 # time to go from 0 to +1
braking_time = 0.3 # time to go from 0 to +1
driver.SetSteeringDelta(render_step_size / steering_time)
driver.SetThrottleDelta(render_step_size / throttle_time)
driver.SetBrakingDelta(render_step_size / braking_time)
driver.SetGains(4.0, 4.0, 4.0) # first-order lag from key target to applied input
# ... and then, when the Irrlicht window is built:
vis.AddSkyBox()
plant.attach(vis)
if INPUT_SOURCE in ("keyboard", "gamepad"):
vis.AttachDriver(driver) # route Irrlicht key/joystick events to the driver
AttachDriver forwards the window's key events - and binds Chrono's gear keys Z X T [ ] for free
A gamepad or wheel is the same class and one more call: SetInputMode(JOYSTICK), with presets that ship with Chrono
For anything else, nothing is wired up for you - which is the next three slides
University of Wisconsin - Madison
11

## Slide 12: Two processes, one UDP contract
Both directions are plain UDP datagrams - two processes, possibly two machines, no shared memory. The return arrow only fires when SEND_FEEDBACK = True.
Operator machine
operator_console.py
Simulation machine
tutorial_HIL_driver.py
→ steering, throttle, braking, gear
speed, RTF, lateral accel, gear ←
University of Wisconsin - Madison
12

## Slide 13: A UDP input source (Lines 219 to 269)
class UdpInput:
"""Receive 'steering,throttle,braking[,gear]' datagrams from an operator.
Non-blocking: the physics loop never waits. No packet since the last step
means the previous target is held (zero-order hold)."""
def __init__(self, port=9870):
self.sock = socket.socket(socket.AF_INET, socket.SOCK_DGRAM)
self.sock.bind(("0.0.0.0", port))
self.sock.setblocking(False)
self.operator_addr = None
self.last = (0.0, 0.0, 0.0)
self.gear_commands = []
def poll(self):
# Drain everything queued and keep only the newest packet. Gear commands
# are the exception: they accumulate, because dropping one loses a shift.
while True:
try:
data, addr = self.sock.recvfrom(256)
except BlockingIOError:
break
fields = data.decode().split(",")
if len(fields) < 3:
continue
try:
s, t, b = (float(x) for x in fields[:3])
except ValueError:
continue
self.last = (s, t, b)
self.operator_addr = addr
if len(fields) > 3 and fields[3] and fields[3] != "-": # PART 6
self.gear_commands.append(fields[3][0])
return self.last
Non-blocking socket, drained every step: the newest packet wins, and an empty queue holds the last value
The operator can be anywhere on the network, and the console has no Chrono dependency at all
University of Wisconsin - Madison
13

## Slide 14: Sample once, hold, then send state back (Lines 710 to 722, 771 to 781)
# PART 4: sample the device ONCE per step and hold it for the step
if device is not None:
smoother.set_target(*device.poll())
smoother.advance(step_size)
smoother.apply_to(driver)
# PART 6: gear commands are events, not levels, so they are applied
# once each rather than held like the three numbers above.
if gearbox is not None:
for command in device.take_gear_commands():
gearbox.command_char(command)
# Get driver inputs (three floats) - this is the whole human-in-the-loop contract
driver_inputs = driver.GetInputs()
# ... and at the end of the same step:
# PART 4: feedback to the operator (speed, RTF, lateral acceleration, applied
# inputs, and since PART 6 the gear)
if SEND_FEEDBACK and device is not None and step_number % render_steps == 0:
acc = (vehicle.GetPointAcceleration(chrono.ChVector3d(0, 0, 0)).y
if vehicle else 0.0)
rtf = vehicle.GetRTF() if vehicle else 0.0
gear = gearbox.describe() if gearbox else plant.status() or "--"
device.send_feedback(
f"{sim_time:.3f},{plant.speed():.3f},{rtf:.3f},{acc:.3f},"
f"{driver_inputs.m_steering:.3f},{driver_inputs.m_throttle:.3f},"
f"{driver_inputs.m_braking:.3f},{gear}")
poll -> smooth -> write, then GetInputs() as before; the physics loop never waits on the device
Feedback goes back at render rate (50 Hz), not every physics step - the human cannot use 333 Hz
University of Wisconsin - Madison
14

## Slide 15: Show Time
Two terminals on one laptop over localhost - or two machines over the network, same code either way
Stop the console mid-drive: the last input is held - what should a real simulator do here?
University of Wisconsin - Madison
15

## Slide 16: Variable 2: what the numbers drive
University of Wisconsin - Madison
16

## Slide 17: PLANT: a car, a rover, a crane
PLANT switches what the same three numbers, from the same devices, are wired into
  "vehicle" a Chrono::Vehicle - steering, throttle, braking, as usual
  "rover" a Viper rover - steering becomes a wheel angle in radians, throttle a commanded wheel speed
  "crane" a gantry crane - steering becomes cross-travel, throttle and braking forward/reverse travel
The rover shows what "the same three numbers" really costs: braking has no meaning there
  ViperDriver has no brake input, so holding the brake releases the drive and it coasts. Real limits show up like this
Neither has a ChVehicle, so ChInteractiveDriver cannot read the keyboard for them - they take UDP, console unchanged
University of Wisconsin - Madison
17

## Slide 18: The crane: no Chrono::Vehicle at all (hil_plants.py 319 to 324)
def apply(self, inputs):
t = self.system.GetChTime()
# Throttle drives forward, braking drives back: two pedals, one axis.
long_cmd = (inputs.m_throttle - inputs.m_braking) * self.MAX_LONG_SPEED
self.long_speed.SetSetpoint(long_cmd, t)
self.cross_speed.SetSetpoint(inputs.m_steering * self.MAX_CROSS_SPEED, t)
Four rigid bodies, two speed motors and a distance constraint - and that apply() is the whole interface to it
The payload swings, with nothing to damp it but the operator, and the console prints the swing angle and the miss distance
Placing it without a swing is a genuinely hard manual task, which is the clearest answer to why a human goes in the loop at all
University of Wisconsin - Madison
18

## Slide 19: Show Time
PLANT = "crane" over udp: put the load on the green pad with the swing under 2 degrees
Then PLANT = "rover" and hold the brake: it coasts rather than stopping
Same loop, same console, same three numbers. Only PLANT changed
University of Wisconsin - Madison
19

## Slide 20: Variable 3: where it happens
University of Wisconsin - Madison
20

## Slide 21: Mcity: driving somewhere real
SCENE = "mcity" swaps the 200 x 200 m patch for a real 32-acre test facility
  road surface driven as a collision mesh; buildings, poles, signal heads drawn from a placement manifest
  MCITY_DETAIL = "ground" | "light" | "full" trades scenery for frame rate - start at "ground" on a laptop
  860 placements cost 230 meshes: one ChVisualShape, added to a body many times, each time with its own frame
Third-party and generated, not shipped: a missing dataset falls back to flat terrain with instructions
Two things that cost time to rediscover:
  Drive the DRAWN geometry: Mcity's OpenDRIVE elevation differs from the road mesh by -0.24 to +0.29 m (5th/95th pct)
  Read the spawn height from the mesh: RigidTerrain raycasts a collision system that does not exist yet and answers 0
University of Wisconsin - Madison
21

## Slide 22: And the one thing that is not a number at all
# A ChDriver carries three numbers, and a gear is not one of them: the
# gearbox belongs to the VEHICLE, so it is reached through the vehicle.
transmission = vehicle.GetTransmission()
transmission.ShiftUp() # or ShiftDown(), SetGear(n)
transmission.asAutomatic().SetDriveMode(...) # D / N / R
transmission.asAutomatic().SetShiftMode(...) # let it shift, or row it
# On the keyboard you write none of this - vis.AttachDriver(driver) binds:
# Z D <-> R X neutral T AUTO <-> MANUAL [ ] down / up
#
# For a device Chrono has never heard of, nothing is wired up. That is the
# point of PART 4: hil_gearbox.Gearbox turns one character off the socket
# into the calls above, and operator_console.py sends it in a 4th field.
A steering value is a LEVEL: re-sent every frame, and a lost packet costs nothing
A gear change is an EVENT: a lost one is a shift that never happened - sent once, on the key-down edge, applied exactly once
That distinction is the last thing this tutorial has to teach, and it is not specific to gears or to Chrono
University of Wisconsin - Madison
22

## Slide 23: Where this goes next
Chrono::HIL (github.com/zzhou292/chrono-HIL): the same three-float interface, scaled up
  SDL steering wheels with force feedback, cumulative real-time timer, multi-vehicle traffic
  ROS 2 and Unity bridges, teleoperation over the network, deformable (SCM) terrain
Chrono::Sensor: cameras/lidar rendered from the vehicle for the operator's screen
Chrono::Synchrono: several humans in the same world, each on their own machine
Takeaways
  Real time in Chrono is soft: spin once per step, and measure the drift
  The human interface is three floats per step, sampled once and smoothed
  Never let the input device block the physics loop
  Levels are held, events are drained - a gear is an event
  Nothing in the pattern needs a vehicle: swap the plant, keep the loop
University of Wisconsin - Madison
23

## Slide 24: Any questions?
University of Wisconsin - Madison
24

## Slide 25
Thank you.
kasha2@wisc.edu
Simulation-Based Engineering Lab
University of Wisconsin - Madison
Lab website: http://sbel.wisc.edu
Chrono website: http://www.projectchrono.org
Source code: https://github.com/projectchrono
Tutorial code + slides: https://github.com/ksha23/chrono-hil-tutorial
University of Wisconsin - Madison
25